## Slide 1: The Histogram-Difference Method (HDM): A simple, topographical method for discriminating neutron/gamma pulses Robert M. French (LEAD-CNRS UMR 5022) Mathieu Thévenin (CEA) Matthieu Hamel (CEA) Eva Montbarbon (CEA)
French, R. M., Thévenin, M., Hamel, M. & Montbarbon, E. (2017). A Histogram-Difference Method (HDM) for Neutron/Gamma Discrimination Using Liquid and Plastic Scintillators. IEEE Transactions on Nuclear Science (in press).
Patent filed: FR1753811
ANIMMA 2017, Liège, June 19-23, 2017

## Slide 2
The Problem
UNLABELED PULSES (neutron OR )
Are there neutrons in the UNLABELED PULSES ?
If so, what percentage?
Pulses are acquired by liquid or plastic scintillators designed to be used in Radiation Portal Monitors.

## Slide 3
Normalized neutron and gamma pulses are supposed to look like this.
Flaska & Pozzi (2006)

## Slide 4
But in reality, they look like this!
Neutrons + gamma pulses = blue
True gamma pulses = red

## Slide 5
After amplitude normalization and peak alignment
-only
n+
The average -only pulse (red) and the average n+ pulse (blue).

## Slide 6
Q-value representation: Each pulse is represented as a pair of real values: (Qtotal , Qtail)

## Slide 7
Q-value representation: Each pulse is represented as a pair of real values: (Qtotal , Qtail)
Qtail
Qtotal

## Slide 8
Traditionally, we create a scatterplot from these values: Qtotal (x-axis) vs Qtail (y-axis).

## Slide 9
HDM adds topography (i.e., includes the number of pulses) to produce histograms

## Slide 10
n+
-only
HDM adds topography (i.e., includes the number of pulses) to produce histograms

## Slide 11
n+ histogram
(16,000 pulses)
-only histogram
(16,000 pulses)
One axis is Qtotal and the other is Qtail
The height represents the number of (Qtotal , Qtail ) pairs in each square of a 150x300 grid.

## Slide 12
A key assumption of HDM
The histogram for any set of N -only pulses, regardless of their source, is essentially the same.
Na-22
Co-60
Offline, we combine pulses from the 3 sources
and create a Reference Set of N -only pulses.
Cs-137

## Slide 13
A toy example of how HDM works
Three key assumptions
All -only histograms with 10 pulses will look exactly like the -only histogram on the left. This is the Reference -only Histogram.
There are exactly the same number of pulses (10) in the -only histogram and the n+ histogram.
Any difference between the -only histogram and the n+ histogram
must be due to neutrons.
Total of ten pulses. Each pulse is represented by an integer between 1 and 5.

## Slide 14
Comparing a Gamma-only spectrum and a Neutron+Gamma spectrum
Since there are exactly 10 pulses in each histogram,
we see that one  pulse with a representation of « 5 » in the -only spectrum
is replaced by
one neutron pulse with a representation of « 2 » in the n+ spectrum.
Remember:
Since all 10-pulse -only histograms are strictly identical,
any difference between the -only histogram and the n+  histogram
must be due to neutrons.

## Slide 15
We conclude that there is (at least) one neutron in the Neutron+Gamma sample.
The n+ sample has at least 10% neutrons.
A toy example of HDM (a total of 10 pulses)
-only histogram
n+ histogram

## Slide 16
No. of pulses
Consider a slice through the real histogram landscape
 histogram
If the new n+ sample is the same size as the -only sample, and contains only gamma pulses, its histogram will closely match the -only histogram.
n+ histogram

## Slide 17
No. of pulses
 histogram
However, any significant divergence from the -only histogram will be caused by neutrons. Recall that there must be the same number of n+ pulses as -only pulses.
n+ histogram
Consider a slice through the real histogram landscape

## Slide 18
Consider a slice through this landscape
Significant divergence from the -only histogram will be caused by neutrons.
This divergence allows us to:
Conclude that neutrons are present in the n+ sample and
Estimate a lower bound for the % of neutrons in the sample.

## Slide 19
A “summed projection” onto the yz-plane of the 3D Q-value histogram of 16,000 -only pulses (red) and 16,000 n+ pulses (blue).
This graph illustrates the key principle of the HDM: the differences with respect to the -only reference histogram (red) are due to the presence of neutrons.
The difference in the two summed projections allows us to determine the approximate minimum percentage of neutrons in the n+ set.

## Slide 20
Results
Using other techniques, this value has been reported elsewhere in the literature to be between 25% and 30%.
For all scintillators the bias is approximately 4%
Scintillator | Neutron estimate (%) Cf-252 | 
BC-501-A | 29.9 | 
E32 | 26 | 
EJ-299-33 | 26.3 | 
EJ-200 | 23.2 | 

## Slide 21
HDM is representation-independent
HDM does not require a single type of pulse representation.
Other possible pulse representations: ToT, Zero-Crossing time, Rising Time, etc.
We tested HDM using an entirely different representation from Q-values, D-values which represent each pulse as its RMS distance to the average of all pulses in the -only Reference Set.

## Slide 22
For all pulses in the -only reference set, S, and in the test set, Sn+, we only consider their values between t0 = 20 and t1=150.
Truncate
20
150
130-value vector
Normalize
1

## Slide 23
We then calculate the average of these 130-value vectors for all pulses in the -only reference set, S. This vector is the centroid pulse, C for S.
For all pulses in S and in Sn+ we calculate the Euclidean distance to C. We call these D-values. For each pulse, its distance to C constitutes its D-value representation.
We bin these D-values to create a -only histogram and an n+ histogram.
The difference between these histograms gives a lower bound on the % of neutrons in the n+ sample.

## Slide 24
Summed projection of Q-value histograms for the -only Reference Set (red) and n+ pulses (blue)
D-value histograms of distances from C for pulses from the -only Reference Set (red) and n+ pulses (blue)
-only
n+
With Q-values HDM gives a lower-bound estimate of 30% neutrons in Cf-252.
With D-values HDM gives a lower-bound estimate of 27% neutrons in Cf-252.
Both of these estimates are within the 25-30% estimates obtained by other methods.

## Slide 25
Small samples
- To test HDM, -only and n+ samples originally consisted of 16,000 pulses.
- Does this method work for much smaller sample sizes?

## Slide 26
The -only Reference Set, S, has 16,000 pulses.
We scale it to have the same total number of pulses as Sn+.
4%
< 1%

## Slide 27
Conclusions
HDM is a simple method for calculating whether there is neutron emission from a given source and, if so, determines a lower bound on the percentage of neutron pulses from that source.
HDM’s results correspond to values found using other, more complex methods.
HDM does not depend on a particular pulse representation.
HDM is computationally efficient.
HDM can easily be implemented in hardware (FPGA).

## Slide 28
Thank you!